## Slide 1: Profiling with Allinea MAP
Geert Jan Bex
(geertjan.bex@uhasselt.be)
License: this presentation is released under the Creative Commons, see http://creativecommons.org/publicdomain/zero/1.0/

## Slide 2: Introduction

## Slide 3: Introduction
Allinea Forge (https://www.allinea.com/)
  Allinea DDT: parallel debugger
  Allinea MAP: parallel profiler
Commercial product
  Floating licence, token based
  64 tokens, e.g.,
    2  2 MAP sessions of 32 processes
    1  MAP + 1  DDT session of 32 processes
    1  DDT session of 64 processes
Analyzing a profile offline: half price

## Slide 4: Supported programming models
Serial applications
Shared memory programming: OpenMP
GPU programming: CUDA
Distributed programming: MPI, UPC
Debugging/profiling at scale: user interface optimized
Weapon of choice for MPI (+ OpenMP)

## Slide 5: Alternatives
Debugging
  Commercial: RogueWave TotalView
  Open source: Eclipse PTP
Profiling
  Open source:
    Scalasca
    Paraver + Extrae

## Slide 6: Profiling

## Slide 7: Methodology
MAP uses sampling (call stack)
  No instrumentation
  Simply compile with -g for details
  Overhead is minimal ( 5-10 % at most)
Works with many MPI implementations
  Intel MPI
  OpenMPI
  MVAPICH
  …

## Slide 8: Startup
$ module load AllineaForge
$ map
Start profiling interactively
```
Load a profile to analyze
Start a job to profile interactively

## Slide 9: Interactive profiling
Run configuration
Remembers between runs
Choose application
Application arguments
Working directory
Configure MPI/OpenMP
Start run/profiling

## Slide 10: Results
Ask your boss for a large screen

## Slide 11: Overview
Vector floating point
No branching
Memory access 74 %

## Slide 12: Time line
Can display many metrics
  CPU instructions
  I/O: disk read/write
  MPI
    Number calls peer-to-peer & collectives/s
    Peer-to-peer & collectives bandwidth
    Send & receive bandwidth
time
processes
Any combination
Zoom by selecting
Very useful to identify run
phases
All view updated!
min, max, mean, s.d. available

## Slide 13: Source code view
Easy to navigate through code
  Go to function definitions in any file
Requires compile with -g
Line based activity
Color coded:
 Communication
 Compute
Code can be folded

## Slide 14: Call stack view
Ordered by % runtime
Navigate to source code
Click to go to code

## Slide 15: Round tripping
From within Allinea MAP
  Edit code
  Rebuild
  Profile
  Commit in version control system
Switch between MAP and DDT

## Slide 16: Interactive profiling via job
Job will run on compute nodes

## Slide 17: Batch profiling via job
Submit job
When done, open profile with MAP
#!/bin/bash –l
#PBS –l nodes=1:ppn=4
#PBS –l walltime=1:00:00
…
map --np 4 --profile --stop-after 3500 \
diffusion.exe 10000 5000 30

## Slide 18: Conclusions

## Slide 19: Conclusions
MAP is excellent for applications with many processes/threads
  Easy to get an overview
However, works well for serial code too
Timeline is valuable tool
Very easy to use, but correct interpretation requires insight
Drawback: limited to number of tokens
  Number of processes
  Concurrent sessions
As any tool, not Swiss army knife
  Use in combination with other tools, e.g., Intel