## Slide 1: HPC efficiency considerations
Geert Jan Bex (geertjan.bex@uhasselt.be)
License: this presentation is released under the Creative Commons, see http://creativecommons.org/publicdomain/zero/1.0/

## Slide 2: Introduction

## Slide 3: Moore's law
In the good, old days…
  CPU clock frequency increased: performance was free lunch
Problems
  Heat dissipation
  Power efficiency
However…
"The number of transistors in a dense integrated circuit doubles approximately every two years".

## Slide 4: Parallelism
Levels
  vectorization
    compiler flags, programmer can/should help
  multicore
    OpenMP/pthreads: programmer's job
  multiple nodes, i.e., distributed
    MPI/CAF/UPC/Chapel: programmer's job
  GPGPU
    CUDA/OpenACC/OpenCL: programmer's job
Hybrid

## Slide 5: Parallel scaling

## Slide 6: Dimensions for scaling
Scaling considered in two dimensions
  solve same problem faster by using more resources
  solve larger problem by using more resources
Weak scaling
Strong scaling

## Slide 7: What you hope/expect for…
strong scaling
weak scaling
Chart: 
| 1 | 2 | 4 | 8 | 16 | 32 | 64 | 128
execution time | 128 | 64 | 32 | 16 | 8 | 4 | 2 | 1
nr. processes
execution time
execution time 
system size
nr. processes
Is this going
to happen?

## Slide 8: Definitions
Parallel speedup for processes:
  Ideally,
Parallel efficiency for processes:
  Ideally,

## Slide 9: Strong scaling: oops!?!
Some parts of a program can not be parallelized (effectively)
  so
  b
  and hence
  so even for one has
Hard limit on speedup due to serial part: Amdahl's law

## Slide 10: Amdahl's law
nr. processes
speedup
Chart: 
| 1 | 2 | 4 | 8 | 16 | 32 | 64 | 128
serial 0.1 | 1 | 1.8182 | 3.0769 | 4.7059 | 6.4 | 7.8049 | 8.7671 | 9.3431
serial 0.01 | 1 | 1.9802 | 3.8835 | 7.4766 | 13.913 | 24.4275 | 39.2638 | 56.3877
serial 0.001 | 1 | 1.998 | 3.988 | 7.9444 | 15.7635 | 31.0378 | 60.207 | 113.5759
perfect | 1 | 2 | 4 | 8 | 16 | 32 | 64 | 128

## Slide 11: It gets worse…
Overhead!
  communication takes time
    finite bandwidth
    non-zero latency
  resource contention
    memory subsystem: L3 cache, RAM, QPI
    network access
Chart: 
| 1 | 2 | 4 | 8 | 16 | 32 | 64 | 128
reality | 1 | 1.8091 | 3.0311 | 4.544 | 5.9376 | 6.6842 | 6.3981 | 4.9512
Amdahl's law | 1 | 1.8182 | 3.0769 | 4.7059 | 6.4 | 7.8049 | 8.7671 | 9.3431
nr. processes
nr. processes

## Slide 12: Picking the sweet spot
Chart: 
| 1 | 2 | 4 | 8 | 16 | 32 | 64 | 128
reality | 1 | 1.8091 | 3.0311 | 4.544 | 5.9376 | 6.6842 | 6.3981 | 4.9512
nr. processes
speedup
Chart: 
| 1 | 2 | 4 | 8 | 16 | 32 | 64 | 128
efficiency | 1 | 0.90456 | 0.75778 | 0.568 | 0.3711 | 0.20888 | 0.099971 | 0.038681
nr. processes
efficiency
sweet spot
sweet spot

## Slide 13: Weak scaling
Consider a system of "size"
  as before
  but now assume is independent of , but
  now choose the number of processes
  and hence
Gustafson's law:
Nice for scientists!

## Slide 14: We love Gustafson
Scientist are interested in
  studying larger systems/bigger data sets
  increasing precision/resolution
  more complex phenomena
  …

## Slide 15: Throughput computing
N independent tasks
Total number of cores n << N
Execution time single task, 1 thread: t1
Execution time single task, n threads: tn
Multithreading or not?
However: memory?

## Slide 16: Computer architecture

## Slide 17: Compute node architecture
DDR3
DDR3
DDR3
DDR3
DDR3
DDR3
DDR3
DDR3
QPI
QPI
core0
L1
L2
Socket 0
NUMA node 0
Socket 1
NUMA node 1
L3
core0
L1
L2
core1
L1
L2
core2
L1
L2
core3
L1
L2
core4
L1
L2
core5
L1
L2
core6
L1
L2
core8
L1
L2
core9
L1
L2
core7
L1
L2
L3
core10
L1
L2
core11
L1
L2
core12
L1
L2
core13
L1
L2
core14
L1
L2
core15
L1
L2
core16
L1
L2
core18
L1
L2
core19
L1
L2
core17
L1
L2
IB
I/O

## Slide 18: Memory

## Slide 19: Memory hierarchy
Data transport takes time!
RAM
  size: 64 GB+
  latency: 150 cycles
L3 cache
  size: 25 MB+
  latency: 50 cycles
L2 cache
  size: 256 kb
  latency: 20 cycles
L1 cache
  size: 32 kb data + 32 kb instruction
  latency: 5 cycles
Bandwidth: 130 GB/s
QPI incurs 10 % loss
on average: 3 MB/core

## Slide 20: Memory hierarchy timings
32 kb
256 kb
16 Mb
L1
L2
L3

## Slide 21: Cache lines
double a[n];
…
for (i = 0; i < n; i++)
f(a[i])
Transport 64 byte at once: RAM  L3  L2  L1
  cache line
  8 double or 16 single precision
Data structure layout is critical!
  access to contiguous data
a[i-1]
a[i]
a[i+1]
a[i+7]
a[i+8]
…
…
…
cache line
not exploited: effective  memory bandwidth/8 or 16
 cache size/8 or 16
cache line

## Slide 22: Cache line timings
stride 16
less work, almost equal time!
memory bound,
equal number
of cache lines
to fetch
int a[n];
…
for (i = 0; i < n; i += K)
a[i] *= 3
less work, less cache lines to fetch

## Slide 23: Multidimensional arrays
Ordering of 2D/3D/… arrays
  by row: C/C++
  by column: Fortran, Matlab
a1,1
a1,2
a1,3
a2,2
a2,3
…
…
a2,1
a1,1
a2,1
a3,1
a2,2
a3,2
…
…
a1,2
row-major
column-major
Access in "wrong" order: performance degradation!

## Slide 24: AoS versus SoA
struct particle {
double x, y, z, m;
int q;
};
struct particle particles[n];
Array of Structs versus Struct of Arrays?
struct particles {
double x[n], y[n], z[n],
m[n];
int q[n];
};
xi
xi+1
xi+2
yi
yi+1
…
…
cache line
cache line
xi
yi
zi
qi
xi+1
…
…
mi
May transport useless data: performance degradation

## Slide 25: Cache associativity: size matters
Lower bits of memory address: slot in cache
L2: 8-way associative, 256 kb
  cache line: 64 byte, so 262144/64 = 4096 slots
  8-way, so 4096/8 = 512 sets, 8 slots each
  when slots are full, eviction from cache, so data 512  64 = 32768 bytes apart competes for slots
L1/L2: 8-way associative L3: 20-way associative
Cache evictions limit reuse, reduce performance!
Cache info:
dmidecode –type 7

## Slide 26: Performance impact
Performance drop
Avoid 2D/3D arrays with sizes 2n
Cache size

## Slide 27: CPU

## Slide 28: Vectorization
Arithmetic operation done on registers
Vector registers for floating point operands: 256 bit wide
  4 double precision
  8 single precision
4 concurrent operations
8 concurrent operations
double precision: 4 registers × 2.5.109 additions × 18 cores × 2 sockets = 360 GFLOPS
Theoretical peak performance!

## Slide 29: (Counter) examples
Can be vectorized
Can not be vectorized
double a[N], b[N], c[N];
for (int i = 0; i < N; i++)
a[i] = a[i] + b[i]*c[i];
double a[N], b[N], c[N];
for (int i = 1; i < N; i++)
a[i] = a[i-1] + b[i]*c[i];
All iterations are independent
Iteration i depends on iteration i - 1
Loop done in chunks of 4

## Slide 30: Compiler flags & directives
GCC compiler family
  gcc –march=corei7-avx –O3 …
  gcc –ftree-vectorize \ –march=corei7-avx –O2 …
  for feedback, use -ftree-vectorizer-verbose=2
Intel compiler family
  icc –xHost –O2 …
  for feedback, use -qopt-report-phase=vec \ -qopt-report=3
Help compiler using, e.g., #pragma omp simd …

## Slide 31: Timings for double precision
Number of operations | Dependent | Independent
1 | 1.0 | 1.0
2 | 2.0 | 1.0
4 | 4.0 | 1.0
8 | 8.2 | 1.0
Timings are unit-less relative numbers
Intel compilers 16.x are very smart

## Slide 32: AVX2
Haswell, Broadwell CPUs: AVX2 instruction set
  Fused multiply/add: a*x + b is single operation
  Integer vector registers: 256 bit wide
  Extra operations for cryptography
Streaming: 1 addition and 1 multiplication/cycle!
Worth to recompile!

## Slide 33: AVX-512
Skylake CPUs: vector registers for floating point operands: 512 bit wide
  8 double precision
  16 single precision
8 concurrent operations
16 concurrent operations
Even more worth to recompile!

## Slide 34: Double promotion
GCC gcc/g++
  -Wdouble-promotion
float area(float radius) {
return 3.1425927*radius*radius;
}
Promoted to double
float area(float radius) {
return 3.1425927f*radius*radius;
}
All float

## Slide 35: Note of caution
Intel compilers: aggressive optimization
  Even at –O2
  Reordering of operations/operands
    May impact precision
  Verify results with -fp-model precise –fp-model source
Potentially severe performance impact!

## Slide 36: Multithreading: false sharing

## Slide 37: Cache lines, again
a[i-1]
a[i]
a[i+1]
a[i+7]
a[i+8]
…
…
…
cache line
RAM
core 0
L1
a[i]
a[i+1]
a[i+7]
…
L2
a[i]
a[i+1]
a[i+7]
…
L3
a[i]
a[i+1]
a[i+7]
…
core 1
L1
a[i]
a[i+1]
a[i+7]
…
L2
a[i]
a[i+1]
a[i+7]
…
cache consistency:
MESI protocol
exclusive
shared
modified
invalid
invalid

## Slide 38: Bad news and good news
Bad news: performance
  degraded by 1.5 to 4
  can be hard to spot, e.g., global variables close in memory
Good news: compilers
  compilers detect many cases, make variables implicitly thread-private
  GCC: -O2 or more
  Intel: -O1 or more
However, compiler won't always remedy,
so avoid false sharing!

## Slide 39: How to avoid?
Use thread-local variables/copies when possible
Align C global variables at cache boundaries, e.g., int counter_t0 __attribute__((aligned(64))); int counter_t1 __attribute__((aligned(64)));
Align Fortran variables at cache boundaries (Intel only), e.g., integer :: counter_t0, counter_t1 !dir$ attributes align:16 :: counter_t0, counter_t1
Pad C struct to multiples of cache line length, e.g., struct data { double x, y, z; double padding[5]; }; struct data pnts[20] __attribute__((aligned(64)));
For Fortran user defined types, use
  SEQUENCE + carefully order members
  avoid SEQUENCE, but use compiler flag -align rec16byte
Cost: larger memory footprint!

## Slide 40: Feedback-guided optimization

## Slide 41: Philosophy
"The proof of the pudding is in the eating"
  Build application with instrumentation
  Run application
    creates profile
  Rebuild application, using profile to guide optimizations
Depends on quality of run: must be representative for general use
  CPU/memory architecture
  input data/parameters
YMMV: expect < 10 %

## Slide 42: GCC compilers
Build with instrumentation
Run as usual
Build using profile
gcc -fprofile-generate -o appl.exe …
gcc -fprofile-use=appl.exe.gcda -o appl.exe …

## Slide 43: Intel compilers
Build with instrumentation
Run as usual
Build using profile
icc -prof-gen -prof-dir=./profs -o appl.exe …
icc -prof-use prof-dir=./profs -ipo -o appl.exe …

## Slide 44: Example
Code illustrating cache hierarchy
improved
pre-fetching

## Slide 45: Conclusion

## Slide 46: Useful references
Gallery of processor cache effects
Avoiding and Identifying False Sharing Among Threads
Vectorization
  A guide to vectorization with Intel C++ compilers
  Auto-vectorization with gcc 4.7
Introduction to High Performance Computing for Scientists and Engineers Georg Hager & Gerhard Wellein Chapman & Hall, 2010
Why has CPU frequency ceased to grow?

## Slide 47: Appendix

## Slide 48: Tools
Profilers
  gprof
  Scalasca
  AllineaForge MAP
  Intel vTune
Hardware information
  lscpu: CPU information, including cache size and NUMA configuration
  lstopo-no-graphics: more detailed cache topology
  Intel mlc: provides memory bandwidth & latency info
Use a profiler, it is the law!

## Slide 49: Latency
Core
L1 cache
5 cycles
L2 cache
20 cycles
L3 cache
50 cycles
RAM
150 cycles
Infiniband
5000 cycles
disk I/O
1000000 cycles
1 cycle
streaming DP fused multiply/add
5 cycles
+ or *
10 cycles
/ or sqrt
20 cycles
exp
40 cycles
**
80 cycles
erf
latency
OpenMP barrier
1500 cycles
compute time
GPGPU
20000 cycles

## Slide 50: Bandwidth
RAM
  ivybridge (dual socket, 10 core): 93 GB/s
  haswell (dual socket, 12 core): 110 GB/s
  broadwell (dual socket, 14 core): 125 GB/s
QPI
  ivybridge: 25 GB/s
  haswell: 30 GB/s
  broadwell: 30 GB/s
GPGPU RAM (GDDR5@750MHz, K40c): 288.0 GB/s
SATA revision 3: 0.6 GB/s
SATA revision 3.2: 2.0 GB/s
SAS 3: 1.2 GB/s
PCI Express 3.0 (16x): 15.75 GB/s
Infiniband QDR 4x: 4.0 GB/s
Infiniband EDR 4x: 12.5 GB/s
Note: bandwidth depends
on message size!